## Slide 1: Cloud-based provisioning of qualified certificates for the German ID card
September 11th 2013
Open Identity Summit 2013, Kloster Banz
Marcel Selhorst

## Slide 2: Agenda
Overview: the German eID card (nPA)
Post Issuance Process
Security Goals and Measures
Status quo and future developments
Live-Demo

## Slide 3: Overview: The German ID Card
    provides „classic“ visual identification as well as online authentication
    secured by EAC 2.0
    Three applications on smartcard:
ePass (ICAO compliant - sovereign use only)
▶ fast electronic access to id data by sovereign agencies within the European Union
▶ contains MRZ data, image and optionally fingerprints
eID (Application for electronic identification - optional)
▶ online- and offline-Identification
▶ pseudonym Login-Functionality
▶ anonymous age and place verification
eSign (Application for qualified electronic signatures - optional)
▶ legally binding signatures for electronic documents (QES)
▶ online and offline usable
▶ initially inactive

## Slide 4: eSign Application: „what you want“
sign-me and the new ID Card enable for the first time on-the-fly post-issuance key generation and certification on an SSCD!
Using the German ID card as a secure signature creation device (SSCD)
  Legally equal to personal signature
  Full control by the citizen
  Signature key is generated and stored on ID card
  Immediate online transmission of the generated certificate to the ID Card
  Deletion of the generated signature key under control of the citizen
  Unlimited (re-)generation of signature keys possible
  Different certificate validity periods possible (e.g., < 1 year up to 10 years)
  All advantages of digital signatures in existing business processes are maintained

## Slide 5: sign-me: the standard of tomorrow
Signature Process from the citizen’s point of view:
one-time registration
receiving unique access code
generate key pair and load certificate
electronically sign documents
one-time registration
for all certificates
 requires eID to read personal data
easy handling
identic layout independent of the service provider selling the certificates
grouping of processes one solution for many processes by grouping the required components into one online application
offline signature creation
already 5 different signature application components available supporting sign-me
uncomplicated workflow
users are guided through the necessary steps to ease the overall loading process
All advantages at a glance

## Slide 6: Preliminary Actions
The following preparations are required before starting the certification process:
    Buy a Comfort Reader: Standard reader with display, keypad and security module for secure key storage  required for signature PIN management  required for generation of qualified signatures
    Buy a certificate from an affiliated online shop Certificates are not sold by the Bundesdruckerei directly but rather by affiliated online shops (currently: card reader manufacturer Reiner SCT)
    Register online to obtain a re-usable authorization code Ensures that even in case of theft only the legitimate card holder can initiate the certification process.

## Slide 7: Registration using eID
eID Service
User with browser,
ID card and „AusweisApp“
3
1
2
4
5

## Slide 8: Post-Issuance Certification Process
The Post-Issuance process consists of
    entering the authorization code (received upon registration)
    setting the signature PIN
    selecting a revocation password (for the hotline)
    loading the certificate in an enhanced eID session (including key generation)
    confirming reception of the certificate (required by German signature law)

## Slide 9: Post-Issuance Certification Process
eID Service
1
2
3
User with browser,
ID card and „AusweisApp“

## Slide 10: Post-Issuance Certification Process
eID Service
1
2
3
4
User with browser,
ID card and „AusweisApp“

## Slide 11: Post-Issuance Certification Process
eID Service
1
2
3
4
5
User with browser,
ID card and „AusweisApp“

## Slide 12: Post-Issuance Certification Process
eID Service
1
2
3
4
5
6
User with browser,
ID card and „AusweisApp“

## Slide 13: Post-Issuance Certification Process
eID Service
1
2
3
7
8
4
5
6
User with browser,
ID card and „AusweisApp“

## Slide 14: Security Goals and Measures of eID
  Protection against malicious chip access
  ▶ Mutual authentication between chip and terminal
  Protection against eavesdropping or manipulation of communication
  ▶ PACE: Password Authenticated Connection Establishment
  ▶ establishment of shared secret by EC-DH via PIN, CAN or MRZ
  ▶ establishment of a symmetric encrypted channel using AES
  Protection against unauthorized access to stored data
    ▶ Access Rights are granted by Federal Office of Administration (BVA)
    ▶ fine granular access rights to dedicated data groups and applications
    ▶ can be further limited by the citizen upon each access
  Assurance of Authenticity of the service provider
    ▶ Short lived certificate ▶ Authentication Certificate is provided to the eID Card ▶ Contains terminal‘s access rights
  Data avoidance and data economy
Embedded World 2013
14

## Slide 15: Security Goals and Measures of sign-me
    stolen ID cards can be revoked temporarily or permanently
        certificates are revoked automatically
        certificates expire along with ID card
    the card‘s authenticity and the citizen‘s identity are checked before generating the certificate
    using one single eID session for
        key generation
        export of signature verification key
        certificate generation and storage on card
         ensures a strong binding between certificate, public key and ID card
    Signing Key Pair Algorithm: ECDSA with Brainpool P256r1 curve

## Slide 16: Status quo and future developments
    System is currently in pilot phase
    Operational phase starting 2014
    Currently in development: signature portal for
        Post-issuance certification
        quick and easy signing of electronic documents
        workflow easily integrable for companies (very little development required)
generate document to be signed
deliver document to sign-me portal
user signs online
signature validation incl. report
document is returned to portal

## Slide 17
Thank You  Live-Demo
  Marcel Selhorst Software Architect Bundesdruckerei GmbH Telefon: +49 30 2598 3243 E-Mail: marcel.selhorst@bdr.de